## Slide 1
8
Disk Storage, Basic File Structures, and Hashing

## Slide 2: 8.1. Physical Storage Systems

## Slide 3: Three-Schema(ANSI-SPARC) Architecture
Notes: Internal schema at the internal level to describe physical storage structures and access paths .
  Typically uses a physical data model.

## Slide 4: Classification of Physical Storage Media
Can differentiate storage into:
  volatile storage:
    loses contents when power is switched off
  non-volatile storage:
    Contents persist even when power is switched off.
    Includes secondary and tertiary storage, as well as batter-backed up main-memory.
Factors affecting choice of storage media include
  Speed with which data can be accessed
  Cost per unit of data
  Reliability

## Slide 5: Storage H ierarch y
CPU Registers
CPU Caches
DRAM
SSD
HDD
Network Storage
Faster Smaller Expensive
Cheaper
Slower Larger
Volatile Random Access Byte- Addressable
Non- Volatile Sequential Access Block- Addressable

## Slide 6: Storage H ierarch y
CPU Registers
CPU Caches
DRAM
SSD
HDD
Network Storage
Faster Smaller Expensive
Cheaper
Slower Larger
Memory
Disk

## Slide 7: Storage Hierarchy (Cont.)
Primary storage: Fastest media but volatile (cache, main memory).
Secondary storage: next level in hierarchy, non-volatile, moderately fast access time
  Also called on-line storage
  E.g., flash memory, magnetic disks
Tertiary storage: lowest level in hierarchy, non-volatile, slow access time
  also called off-line storage and used for archival storage
  e.g., magnetic tape, optical storage
  Magnetic tape
    Sequential access, 1 to 12 TB capacity
    A few drives with many tapes
    Juke boxes with petabytes (1000’s of TB) of storage

## Slide 8: ACCESS TIM ES
0.5 ns | L1 Cache Ref
7 ns | L2 Cache Ref
100 ns | DRAM
150,000 ns | SSD
10,000,000 ns | HDD
~30,000,000 ns | Network Storage
1,000,000,000 ns | Tape Archives
0.5 sec
7 sec
100 sec
1.7 days
16.5 weeks
11.4 months
31.7 years
[Source]
For comparison Let 1 ns = 1 sec.

## Slide 9: Jim Gray’s Storage Latency Analogy: How Far Away is the Data?
Registers
On Chip Cache
On Board Cache
Memory
Disk
1ns
2
10
100
Tape /Optical
Robot
10
9
10
6
Sacramento
Lecture Hall
This Room
My Head
10 min
1.5 hr
2 Years
1 min
Pluto
2,000 Years
Andromeda



## Slide 10: Secondary Storage Devices
Formatting
  Divides tracks into equal-sized disk blocks
  Blocks separated by interblock gaps
Data transfer in units of disk blocks
  Hardware address supplied to disk I/O hardware
Buffer
  Used in read and write operations
Read/write head
  Hardware mechanism for read and write operations

## Slide 11: Magnetic Hard Disk Mechanism
Schematic diagram of magnetic disk drive
Photo of magnetic disk drive

## Slide 12: Sectors on a Disk

## Slide 13: Magnetic Disks
Read-Write head
Surface of platter divided into circular tracks
  Over 50K-100K tracks per platter on typical hard disks
Each track is divided into sectors.
  A sector is the smallest unit of data that can be read or written.
  Sector size typically 512 bytes
  Typical sectors per track:
    500 to 1000 (on inner tracks) to 1000 to 2000 (on outer tracks)
Head-disk assemblies
  multiple disk platters on a single spindle (1 to 5 usually)
  one head per platter, mounted on a common arm.
Cylinder i consists of ith track of all the platters
Notes: Mention: checksums, bad sector remapping

## Slide 14: Magnetic Disks
To read/write a sector
  disk arm swings to position head on right track
  platter spins continually;
  data is read/written as sector passes under head
Notes: Mention: checksums, bad sector remapping

## Slide 15: Magnetic Disks (Cont.)
Disk controller – interfaces between the computer system and the disk drive hardware.
  accepts high-level commands to read or write a sector
  initiates actions such as moving the disk arm to the right track and actually reading or writing the data
  Computes and attaches checksums to each sector to verify that data is read back correctly
    If data is corrupted, with very high probability stored checksum won’t match recomputed checksum
  Ensures successful writing by reading back sector after writing it
  Performs remapping of bad sectors

## Slide 16: Performance Measures of Disks
Access time – the time it takes from when a read or write request is issued to when data transfer begins. Consists of:
  Seek time – time to reposition the arm over the correct track.
    4 to 10 milliseconds on typical disks
  Rotational latency – time to put the sector under the head.
    4 to 11 milliseconds on typical disks (5400 to 15000 r.p.m.)
Data-transfer rate – the rate at which data can be retrieved from or stored to the disk.
  50 to 200 MB per second max rate, lower for inner tracks
Notes:   Seek time – time it takes to reposition the arm over the correct track.
    Average seek time is 1/2 the worst case seek time.
      Would be 1/3 if all tracks had the same number of sectors, and we ignore the time to start and stop arm movement
    4 to 10 milliseconds on typical disks
  Rotational latency – time it takes for the sector to be accessed to appear under the head.
    4 to 11 milliseconds on typical disks (5400 to 15000 r.p.m.)
    Average latency is 1/2 of the above latency

## Slide 17: Performance Measures (Cont.)
Disk block is a logical unit for storage allocation and retrieval
  4 to 16 kilobytes typically
    Smaller blocks: more transfers from disk
    Larger blocks: more space wasted due to partially filled blocks
Sequential access pattern
  Successive requests are for successive disk blocks
  Disk seek required only for first block
Random access pattern
  Successive requests are for blocks that can be anywhere on disk
  Each access requires a seek
  Transfer rates are low since a lot of time is wasted in seeks
I/O operations per second (IOPS)
  Number of random block reads that a disk can support per second
  50 to 200 IOPS on current generation magnetic disks

## Slide 18: Performance Measures (Cont.)
Mean time to failure (MTTF) – the average time the disk is expected to run continuously without any failure.
  Probability of failure of new disks is quite low, corresponding to a “theoretical MTTF” of 500,000 to 1,200,000 hours for a new disk (57 to 136 years)
    E.g., an MTTF of 1,200,000 hours for a new disk means that given 1000 relatively new disks, on an average one will fail every 1200 hours.
Most disks have an expected life span of about 5 years and have significantly higher rates of failure once they become more than a few years old.
    MTTF decreases as disk ages

## Slide 19: Solid State Device Storage
Sometimes called flash storage
Main component: controller
Set of interconnected flash memory cards
No moving parts
Data less likely to be fragmented:
  any address is directly addressable
Faster in terms of access time and provides higher transfer rates than HDDs
More costly than HDDs
DRAM-based SSDs available: Faster access times than flash

## Slide 20: Flash Storage
NAND flash
  used widely for storage, cheaper than NOR flash
  requires page-at-a-time read (page: 512 bytes to 4 KB)
    20 to 100 microseconds for a page read
    Not much difference between sequential and random read
  Page can only be written once: Must be erased to allow rewrite
Solid state disks
  Use standard block-oriented disk interfaces, but store data on multiple flash storage devices internally
  Transfer rate of
    up to 500 MB/sec using SATA, and
    up to 3 GB/sec using NVMe PCIe
Is this always true?

## Slide 21: Flash Storage (Cont.)
Erase happens in units of erase block
  Takes 2 to 5 millisecs
  Erase block typically 256 KB to 1 MB (128 to 256 pages)
Remapping of logical page addresses to physical page addresses avoids waiting for erase
Flash translation table tracks mapping
  remapping carried out by flash translation layer
After 100,000 to 1,000,000 erases, erase block becomes unreliable and cannot be used
  wear leveling
Notes: Where is FTL stored? How is it reconstructed on system startup?
How to track number of erases per block (extra storage per block)

## Slide 22: SSD Performance Metrics
Random reads/writes per second
  Typical 4 KB reads: 10,000 reads per second (10,000 IOPS)
  Typical 4KB writes: 40,000 IOPS
  SSDs support parallel reads
    Typical 4KB reads:
      100,000 IOPS with 32 requests in parallel (QD-32) on SATA
      350,000 IOPS with QD-32 on NVMe PCIe
    Typical 4KB writes:
      100,000 IOPS with QD-32, even higher on some models
Data transfer rate for sequential reads/writes
  400 MB/sec for SATA3, 2 to 3 GB/sec using NVMe PCIe
Hybrid disks: combine small amount of flash cache with larger magnetic disk
Notes: QD : Queue depth => refers to the number of outstanding access operations.

## Slide 23: Storage Class Memory
3D-XPoint memory technology pioneered by Intel
Available as Intel Optane
  SSD interface shipped from 2017
    Allows lower latency than flash SSDs
  Non-volatile memory interface announced in 2018
    Supports direct access to words, at speeds comparable to main-memory speeds

## Slide 24: Magnetic Tapes
Hold large volumes of data
  Few GB for DAT (Digital Audio Tape) format, 10-40 GB with DLT (Digital Linear Tape) format, 100 GB+ with Ultrium format, and 330 GB with Ampex helical scan format
  Transfer rates from few to 10s of MB/s
Tapes are cheap, but cost of drives is very high
Very slow access time in comparison to magnetic and optical disks
  limited to sequential access.
  Some formats (Accelis) provide faster seek (10s of seconds) at cost of lower capacity
Used mainly for backup, for storage of infrequently used information, and as an off-line medium for transferring information from one system to another.
Tape jukeboxes used for very large capacity storage
  Multiple petabyes (1015 bytes)

## Slide 25: Secondary Storage Devices
Disk controller
  Interfaces disk drive to computer system
  Standard interfaces
    SATA
    SCSI
      SAS
    NVMe

## Slide 26: SATA
Serial ATA (SATA, abbreviated from Serial AT Attachment) is a computer bus interface that connects host bus adapters to mass storage devices such as hard disk drives, optical drives, and solid-state drives.
Serial ATA succeeded the earlier Parallel ATA (PATA) standard to become the predominant interface for storage devices.
Revisions
Encoding overhead: 8b/10b
SATA revision 1.0
  1.5 Gbit/s, 150 MB/s, Serial ATA-150
SATA revision 2.0
  3 Gbit/s, 300 MB/s, Serial ATA-300)
SATA revision 3.0
  6 Gbit/s, 600 MB/s, Serial ATA-600

## Slide 27
2.5-inch SATA drive on top of a 3.5-inch SATA drive
SATA 2 3 Gbit/s connectors on a computer motherboard
SATA 3 6 Gbit/s host controller, a PCI Express ×1 card

## Slide 28: SCSI: Small Computer System Interface ( “Scuzzy”)
The SCSI standards define commands, protocols, electrical, optical and logical interfaces.
Bus terminator with top cover removed
Parallel SCSI connectors
Notes: Clock skew (timing skew) is a phenomenon in synchronous digital circuit systems in which the same sourced clock signal arrives at different components at different times. The instantaneous difference between the readings of any two clocks is called their skew.

## Slide 29: SCSI: Small Computer System Interface ( “Scuzzy”)
Modern SCSI
‌Break from the traditional parallel SCSI bus and perform data transfer via serial communications using point-to-point links.
Serial Attached SCSI (SAS)
SCSI-over-Fibre Channel Protocol (FCP)
USB Attached SCSI (UAS)‍
Notes: Clock skew (timing skew) is a phenomenon in synchronous digital circuit systems in which the same sourced clock signal arrives at different components at different times. The instantaneous difference between the readings of any two clocks is called their skew.

## Slide 30: SCSI: Small Computer System Interface ( “Scuzzy”)
Although much of the SCSI documentation talks about the parallel interface, all modern development efforts use serial interfaces.
Serial interfaces have a number of advantages over parallel SCSI, including
  higher data rates,
  simplified cabling,
  longer reach,
  improved fault isolation and
  full-duplex capability.
Reason for the shift clock skew issue of high speed parallel interfaces,
  makes the faster variants of parallel SCSI susceptible to problems caused by cabling and termination.
SAS 1.1 | 3 Gbit/s | 8b10b | 300 MB/s 2,400 Mbit/s
SAS 2.1 | 6 Gbit/s |  | 600 MB/s 4,800 Mbit/s
SAS 3.0 | 12 Gbit/s |  | 1,200 MB/s 9,600 Mbit/s
SAS 4.0 | 22.5 Gbit/s | 128b150b | 2,400 MB/s 19,200 Mbit/s
Notes: Clock skew (timing skew) is a phenomenon in synchronous digital circuit systems in which the same sourced clock signal arrives at different components at different times. The instantaneous difference between the readings of any two clocks is called their skew.
All parallel SCSI units use terminators. SCSI is primarily used for storage and backup. An active terminator is a type of single ended SCSI terminator with a built-in voltage regulator to compensate for variations in terminator power.

## Slide 31: NVM Express (NVMe)
NVM Express (NVMe) or Non-Volatile Memory Host Controller Interface Specification (NVMHCIS)
  is an open, logical-device interface specification for accessing a computer's non-volatile storage media attached via PCI Express (PCIe) bus.
By its design, NVM Express allows host hardware and software to:
  Fully exploit the levels of parallelism possible in modern SSDs.
  As a result, NVM Express reduces I/O overhead and brings various performance improvements

## Slide 32: PCI Express link performance
Version | Intro- duced | Line code | Transfer rate | Throughput |  |  |  | 
 |  |  |  | ×1 | ×2 | ×4 | ×8 | ×16
1.0 | 2003 | 8b/10b | 2.5 GT/s | 0.250 GB/s | 0.500 GB/s | 1.000 GB/s | 2.000 GB/s | 4.000 GB/s
2.0 | 2007 | 8b/10b | 5.0 GT/s | 0.500 GB/s | 1.000 GB/s | 2.000 GB/s | 4.000 GB/s | 8.000 GB/s
3.0 | 2010 | 128b/130b | 8.0 GT/s | 0.985 GB/s | 1.969 GB/s | 3.938 GB/s | 7.877 GB/s | 15.754 GB/s
4.0 | 2017 | 128b/130b | 16.0 GT/s | 1.969 GB/s | 3.938 GB/s | 7.877 GB/s | 15.754 GB/s | 31.508 GB/s
5.0 | 2019 | 128b/130b | 32.0 GT/s | 3.938 GB/s | 7.877 GB/s | 15.754 GB/s | 31.508 GB/s | 63.015 GB/s
6.0 (planned) | 2021 | 128b/130b + PAM-4 + ECC | 64.0 GT/s | 7.877 GB/s | 15.754 GB/s | 31.508 GB/s | 63.015 GB/s | 126.031 GB/s

## Slide 33: NVM Express (NVMe)
Intel SSD 750 series, an SSD that uses NVM Express, in form of a PCI Express 3.0 ×4 expansion card

## Slide 34: NVM Express (NVMe)
https://nvmexpress.org/

## Slide 35: NVM Express (NVMe)
Notes: IOPS (Input/Output Operations Per Second, pronounced i-ops) is a common performance measurement used to benchmark computer storage devices like hard disk drives (HDD), solid state drives (SSD), and storage area networks (SAN)

## Slide 36: Storage Interfaces
Disk interface standards families
  SATA (Serial ATA)
    SATA 3 supports data transfer speeds of up to 6 gigabits/sec
  SAS (Serial Attached SCSI)
    SAS Version 3 supports 12 gigabits/sec
  NVMe (Non-Volatile Memory Express) interface
    Works with PCIe connectors to support lower latency and higher transfer rates
    Supports data transfer rates of up to 24 gigabits/sec
Disks usually connected directly to computer system
In Storage Area Networks (SAN), a large number of disks are connected by a high-speed network to a number of servers
In Network Attached Storage (NAS) networked storage provides a file system interface using networked file system protocol, instead of providing a disk system interface

## Slide 37
Optimization of Disk Block Access

## Slide 38: Techniques for efficient data access
Data buffering
  new data can be held in a buffer while old data is processed
Reading data ahead of request
  blocks from the rest of the track can also be read even though they may not have been requested yet.
  in anticipation that they will be requested soon
Use of log disks to temporarily hold writes
  A disk devoted to writing a sequential log of block updates
  Used exactly like nonvolatile RAM
    Write to log disk is very fast since no seeks are required

## Slide 39: Techniques for efficient data access
Proper scheduling of I/O requests
  Schedule so that the arm moves only in one direction and picks up the blocks along its movement.
  Disk-arm-scheduling algorithms re-order block requests so that disk arm movement is minimized
Example:
  Elevator Algorithm: mimics the behavior of an elevator that schedules requests on multiple floors in a proper sequence.

## Slide 40: Techniques for efficient data access
File organization
  Allocate blocks of a file in as contiguous a manner as possible
  Files may get fragmented
    E.g., if free blocks on disk are scattered, and newly created file has its blocks scattered over the disk
    Sequential access to a fragmented file results in increased disk arm movement
    Some systems have utilities to defragment the file system, in order to speed up file access
Notes: keep related data on contiguous blocks

## Slide 41: Techniques for efficient data access
Nonvolatile Write Buffers
Use of SSDs or flash memory for recovery purposes
  involves writing the updates to a non-volatile SSD buffer, which may be a flash memory or battery-operated DRAM.
  Both operate at must faster speeds.
  The disk controller then updates the data file during its idle time and also when the buffer becomes full.
  Writes can be reordered to minimize disk arm movement