## Slide 1
8
Disk Storage, Basic File Structures, and Hashing

## Slide 2: 8.5 RAID

## Slide 3: RAID
RAID: Redundant Arrays of Independent Disks
  disk organization techniques that manage a large numbers of disks, providing a view of a single disk of
    high capacity and high speed by using multiple disks in parallel,
    high reliability by storing data redundantly, so that data can be recovered even if a disk fails

## Slide 4: RAID
The chance that some disk out of a set of N disks will fail is much higher than the chance that a specific single disk will fail.
  E.g., a system with 100 disks, each with MTTF of 100,000 hours (approx. 11 years), will have a system MTTF of 1000 hours (approx. 41 days)
  Techniques for using redundancy to avoid data loss are critical with large numbers of disks

## Slide 5: Improvement of Reliability via Redundancy
Redundancy
  store extra information that can be used to rebuild information lost in a disk failure
E.g., Mirroring (or shadowing)
  Duplicate every disk. Logical disk consists of two physical disks.
  Every write is carried out on both disks
    Reads can take place from either disk

## Slide 6: Improvement of Reliability via Redundancy
Redundancy: E.g., Mirroring (or shadowing)
If one disk in a pair fails, data still available in the other
  Data loss would occur only if a disk fails, and its mirror disk also fails before the system is repaired
    Probability of combined event is very small
Mean time to data loss depends on mean time to failure, and mean time to repair
  E.g., MTTF of 100,000 hours, mean time to repair of 10 hours gives mean time to data loss of 500*106 hours (or 57,000 years) for a mirrored pair of disks (ignoring dependent failure modes)
Notes: Probability of combined event is very small Except for dependent failure modes such as fire or building collapse or electrical power surges

## Slide 7: Improvement in Performance via Parallelism
Two main goals of parallelism in a disk system:
  1. Load balance multiple small accesses to increase throughput
  2. Parallelize large accesses to reduce response time.
Improve transfer rate by striping data across multiple disks.

## Slide 8: Improvement in Performance via Parallelism
Bit-level striping – split the bits of each byte across multiple disks
  In an array of eight disks, write bit i of each byte to disk i.
  Each access can read data at eight times the rate of a single disk.
  But seek/access time worse than for a single disk
    Bit level striping is not used much any more
Block-level striping – with n disks, block i of a file goes to disk (i mod n) + 1
  Requests for different blocks can run in parallel if the blocks reside on different disks
  A request for a long sequence of blocks can utilize all disks in parallel

## Slide 9: Disk reliability: why RAID technology?
Hard drive performance lags CPU performance
Hard drive reliability is poor
RAID can boost both performance and reliability of disks

## Slide 10: What does RAID provide
Performance
  Parallelism
  Load Balancing
Availability
  Redundancy:
    Mirroring, or Striping with Parity
Flexibility
  Selectable Performance/Availability/Cost

## Slide 11: What is RAID?
Redundant Array of Independent Disks (a.k.a. “Disk Array”)
  Originally: Redundant Array of Inexpensive Disks
  Multiple drives, single host disk unit
Provides opportunity to increase:
  Performance via Parallelism
  Data Availability via Redundancy
Cheap cost via commodity disks

## Slide 12: History of RAID
Original paper:
A Case for Redundant Arrays of Inexpensive Disks (RAID) by D. Patterson, G. Gibson, R. Katz - 1987
Presented 6 types of RAID solutions:
  RAID 0 to RAID 5
Companies afterward introduced several more RAID 6, 10, etc.

## Slide 13: RAID 0
Spread data over multiple disk drives:
  STRIPING
Advantage
  Simple to implement
  Fast
Disadvantage
  Very unreliable: RAID 0 with n disks has MTTF equal to 1/n of MTTF of a single disk

## Slide 14: RAID 0
Each drive stores a consecutive chunk of data (chunk size is configurable - usually 1 sector)
If any disk fails, all data is corrupted
Parity
Drive
5
Chunk 2
Chunk 7
Chunk 12
Chunk 17
Chunk 22
Chunk 0
Chunk 5
Chunk 10
Chunk 15
Chunk 20
Chunk 3
Chunk 8
Chunk 13
Chunk 18
Chunk 23
Chunk 4
Chunk 9
Chunk 14
Chunk 19
Chunk 24
Chunk 1
Chunk 6
Chunk 11
Chunk 16
Chunk 21
Drive
4
Drive
3
Drive
2
Drive
1

## Slide 15: RAID 1
Each drive stores same data, one copy per drive:
  MIRRORING
Advantages
  Simple to implement
  Fault-tolerant
Disadvantage
  Requires n times the disk capacity of normal file systems, where n is the number of replications (= disks)

## Slide 16: RAID 2
Data is striped at 1 bit granularity
In addition, we use error correcting code (detect 2, correct 1 bit error) to protect from failures
Provides both BANDWIDTH and RELIABILITY
But: you need a lot of disks!

## Slide 17: RAID 2
1 bit

## Slide 18: RAID 3
Data is striped at 1 byte granularity
In addition, one disk is dedicated to store 1 parity byte for each stripe
Requires N+1 disk drives
  N drives contain data – striped with 1 byte granularity
  Parity drive contains exclusive or of these N fragments
  p[k] = b[k,1]  b[k,2]  ...  b[k,N]

## Slide 19: RAID 3
Improves over RAID 2:
  Parity instead of ECC: requires fewer drives and can still recover one disk if it knows which disk failed
  Coarser store granularity
Parity
Drive
5
Byte 2
Byte 6
Byte 10
Byte 14
Byte 18
Byte 0
Byte 4
Byte 8
Byte 12
Byte 16
Byte 3
Byte 7
Byte 11
Byte 15
Byte 19
Parity
Parity
Parity
Parity
Parity
Byte 1
Byte 5
Byte 9
Byte 13
Byte 17
Drive
4
Drive
3
Drive
2
Drive
1

## Slide 20: RAID 4
Same as RAID 3 but data is stored in chunks, larger than a byte
Usually 1 sector long
Improves on store/read performance
Same performance bottleneck as 3:
  all loads and stores need to access the same disk

## Slide 21: RAID 5
RAID 5 similar to 4, but removes the bottleneck on the parity disk
Parity bytes are stored in different disks for different stripes
RAID-5 distributes the parity blocks among the N+1 drives
Advantages:
  Multiple read/write operations in parallel are possible
  Fault tolerant against 1 disk failure

## Slide 22: RAID 5
25% parity
75% data

## Slide 23: RAID 5 still has one issue
SMALL WRITE PROBLEM of RAID 5:
Happens when we want to update a single block
  Block belongs to a stripe
  How can we compute the new value of the parity block
...
b[k+1]
p[k]
b[k+2]
b[k]

## Slide 24: First Solution
Read values of N-1 other blocks in stripe
Recompute
p[k] = b[k]  b[k+1]  ...  b[k+N-1]
Solution requires
  N-1 reads
  2 writes (new block and parity block)

## Slide 25: Better Solution
Assume we want to update block b[m]
Read old values of b[m] and parity block p[k]
Compute
p[k] = new b[m]  old b[m]  old p[k]
Solution requires
  2 reads (old values of block and parity block)
  2 writes (new block and parity block)

## Slide 26: Better solution illustrated
1. Read
old data.
Old
2.
Write new data
Old P.
3.
XOR old and new data to create Partial Product
5.
XOR old parity with partial product, writing out result as new parity
P. P.
} XOR
} XOR
New P.
Chunk 1
Chunk 2
Chunk 3
Drive
5
Chunk 0
Parity
Drive
4
Drive
3
Drive
2
Drive
1
4.
Read
old parity data
New

## Slide 27: RAID Review
RAID 0 - Data striping, Non-redundant.
  High Performance, Low Reliability
RAID 1 - Mirroring
  Moderate Performance, Expensive High Reliability
RAID 4 - Striping, single parity disk.
  High Bandwidth Performance, Cheap Availability
RAID 5 - Striping, rotating parity disk.
  High Throughput Performance, Cheap Availability

## Slide 28: RAID 6
Data striping with two rotating parity disks
Advantage
  Higher reliability: can recover from the failure of 2 disks
Disadvantage:
  Cost

## Slide 29: RAID 6

## Slide 30: Additional improvements
Hot spare:
  Used to compute (recover) data when one disk fails. After data is recomputed, the hot spare replaces the failed disk
Nested or hybrid RAID
  Nesting of (usually) two RAID levels
  E.g.: RAID 10 = RAID 1 of disks organized in RAID 0 structure
Implementation: can be HW or SW (cheaper)
  Linux has drivers to manage disks in RAID fashion

## Slide 31: RAID Summary
Goal: Reducing performance gap between CPU and I/O
Data availability also a priority
RAID meets the I/O challenge:
  Performance via parallelism
  Data availability via redundancy
  Flexibility via multiple RAID levels, each offer unique performance/availability/cost tradeoffs

## Slide 32: Choice of RAID Level
Factors in choosing RAID level
  Monetary cost
  Performance: Number of I/O operations per second, and bandwidth during normal operation
  Performance during failure
  Performance during rebuild of failed disk
    Including time taken to rebuild failed disk
RAID 0 is used only when data safety is not important
  E.g., data can be recovered quickly from other sources

## Slide 33: Choice of RAID Level (Cont.)
Level 1 provides much better write performance than level 5
  Level 5 requires at least 2 block reads and 2 block writes to write a single block, whereas Level 1 only requires 2 block writes
Level 1 had higher storage cost than level 5
Level 5 is preferred for applications where writes are sequential and large (many blocks), and need large amounts of data storage
RAID 1 is preferred for applications with many random/small updates
Level 6 gives better data protection than RAID 5 since it can tolerate two disk (or disk block) failures
  Increasing in importance since latent block failures on one disk, coupled with a failure of another disk can result in data loss with RAID 1 and RAID 5.

## Slide 34: Hardware Issues
Software RAID: RAID implementations done entirely in software, with no special hardware support
Hardware RAID: RAID implementations with special hardware
  Use non-volatile RAM to record writes that are being executed
  Beware: power failure during write can result in corrupted disk
    E.g., failure after writing one block but before writing the second in a mirrored system
    Such corrupted data must be detected when power is restored
      Recovery from corruption is similar to recovery from failed disk
      NV-RAM helps to efficiently detected potentially corrupted blocks
        Otherwise all blocks of disk must be read and compared with mirror/parity block

## Slide 35: Hardware Issues (Cont.)
Latent failures: data successfully written earlier gets damaged
  can result in data loss even if only one disk fails
Data scrubbing:
  continually scan for latent failures, and recover from copy/parity
Hot swapping: replacement of disk while system is running, without power down
  Supported by some hardware RAID systems,
  reduces time to recovery, and improves availability greatly
Many systems maintain spare disks which are kept online, and used as replacements for failed disks immediately on detection of failure
  Reduces time to recovery greatly
Many hardware RAID systems ensure that a single point of failure will not stop the functioning of the system by using
  Redundant power supplies with battery backup
  Multiple controllers and multiple interconnections to guard against controller/interconnection failures